## Slide 1
ROBOTICS SOFTWARE ENGINEER · TECHNICAL ASSESSMENT
TurtleBot3
Pose Controller
A continuous closed-loop controller in ROS 2 (Python) that drives the robot to a commanded (x, y, yaw) — and curves onto it instead of stopping and turning.
ROS 2 · Python · differential drive · no Nav2
Notes: Quick intro - I built a from-scratch pose controller for TurtleBot3 in ROS 2. The whole story is that it curves smoothly onto a commanded pose and stops on the mark — no Nav2.

## Slide 2
01 / THE TASK
Reach a commanded pose — smoothly
Pose Controller
A ROS 2 service accepts a target x, y, yaw and drives the robot there using odometry feedback, publishing velocities on /cmd_vel.
→ Closed loop on odometry — the controller always works from where the robot actually is.
→ Control law written from first principles — no Nav2 or high-level planning stack.
THE CONSTRAINT THAT SHAPES EVERYTHING
Continuous motion
Drive and rotate at the same time — a single smooth curve onto the goal. No discrete rotate → drive → rotate.
±5 cm
position
±5°
orientation
Notes: The functional ask is straightforward — a service that takes a target pose and drives there on odometry feedback. The interesting engineering constraint is continuous motion - it must curve, not rotate-drive-rotate, and land inside 5cm / 5deg.

## Slide 3
02 / SCOPE
Deliverables
Pose Controller
TECHNICAL EXPLANATION — COVERED IN THIS DECK
✓ Control approach slides 05–07
✓ How pose errors are computed slide 05
✓ How velocity commands are generated slide 06
✓ Assumptions made slide 09
✓ Known limitations slide 10
SUBMITTED WITH THE REPOSITORY
Source code
Git repo — ROS 2 workspace, pose_controller package, all sources.
README
Install deps · run the sim · start the node · call the service.
Demonstration
Screen recording of three target poses (results on slide 08).
Notes: This slide maps the brief to the deck so the panel can see every required item is covered. The five explanation items live in this presentation; code, README and the demo recording ship with the repository.

## Slide 4
03 / ARCHITECTURE
Feedback loop
Pose Controller
Client
service caller
/move_to_pose
returns on arrival
pose_controller
● 20 Hz control loop
● MultiThreadedExecutor
● polar control law
● saturation + slew limit
/cmd_vel
geometry_msgs/Twist
TurtleBot3
Gazebo Harmonic
/odom · nav_msgs/Odometry
pkg · pose_controller_interfaces (ament_cmake) — MoveToPose.srv
pkg · pose_controller (ament_python) — node · math · launch · tests
Notes: Two packages - an interfaces package for the MoveToPose service, and the controller package. The loop is closed - odom in, cmd_vel out, on a 20Hz timer under a MultiThreadedExecutor so the service call can block until arrival without starving the loop.

## Slide 5
04 / FRAMES & CONVENTIONS
ROS logic
Pose Controller
x
forward
y
left
z
up
yaw +
REP-103 · right-handed
· Robot spawns at the odom origin — x = 0, y = 0, yaw = 0. The target pose is interpreted in that same frame.
· Yaw is positive counter-clockwise about +z.
· Odometry orientation is a quaternion → reduced to a single yaw for the planar robot.
· All angles wrapped to (−π, π] so errors never take the long way around ±180°.
· Differential-drive (unicycle) model: only forward velocity v and turn rate ω are commandable — no sideways motion.
Notes: Standard ROS conventions throughout — REP-103, right-handed, yaw positive CCW. Robot spawns at the odom origin and targets are interpreted in that same frame. I reduce the odom quaternion to a single yaw for the planar robot and wrap all angles to keep errors taking the short way round.

## Slide 6
05 / POSE ERRORS
Error calculation
Pose Controller
robot
goal
ρ
heading θ
α
θ_goal
β
dx = x_goal − x
dy = y_goal − y
ρ = hypot(dx, dy)
α = wrap(atan2(dy, dx) − θ)
β = wrap(θ_goal − atan2(dy, dx))
ρ how far the goal point is [m]
α how much to turn to point at the goal [rad]
β extra turn so the final heading equals θ_goal [rad]
Notes: The error is described in polar form relative to the goal. Rho is distance. Alpha is the heading error — how much to turn to point at the goal. Beta is the extra turn so the final heading matches the requested yaw. Everything downstream is built from these three.

## Slide 7
06 / VELOCITY COMMANDS
Control law
Pose Controller
x* y* θ*
+
−
Pose error
ρ · α · β
Control law
v , ω
TurtleBot3
unicycle plant
odometry feedback · x, y, θ
v = k_ρ · ρ · cos(α) # linear velocity
ω = k_α · α + k_β · β # angular velocity
Why it's continuous
v and ω are non-zero together → the robot curves onto the goal. cos(α) trims forward speed when misaligned, and allows a gentle reverse if the goal is behind.
POST-PROCESSING FOR A REAL PLATFORM
· Saturate to TB3 limits — ≤ 0.20 m/s, ≤ 1.6 rad/s
· Slew-rate (accel) cap so commands ramp → smooth, stable
· Terminal settle — within 5 cm, hold position and finish yaw with ω = k_yaw · err
Notes: A single continuous control law — the Siegwart polar pose controller. v and omega are non-zero together, so the robot curves onto the goal. cos(alpha) trims forward speed when misaligned and even allows a gentle reverse if the goal is behind. Then I saturate to platform limits and slew-rate limit so motion ramps smoothly.

## Slide 8
07 / STABILITY & TUNING
Stability
Pose Controller
LYAPUNOV CONDITIONS · SIEGWART 3.6.2
k_ρ > 0
k_β < 0
k_α − k_ρ > 0
GAINS USED
k_ρ = 0.45 k_α = 1.20
k_β = −0.45 k_yaw = 1.50
Tolerances chosen inside spec
Stop at 4 cm (< 5) and 4° (< 5), held for 5 cycles before declaring success — margin against jitter at the boundary.
No recompile to retune
Every gain and tolerance is a ROS 2 parameter in config/pose_controller.yaml.
Notes: The gains aren't arbitrary — they satisfy the Lyapunov stability conditions from Siegwart. Tolerances are set inside spec for margin and held for several cycles before declaring success. Everything is a ROS parameter, so retuning never needs a recompile.

## Slide 9
08 / RESULTS
All three poses, within tolerance
Pose Controller
x
y
start
1.0, 0.5, 45°
−1.0, 0.8, 90°
0.5, −0.5, −90°
TARGET | FINAL | ERROR | 
1.0, 0.5, 45° | 0.980, 0.480, 44.98 | 2.9 cm · 0.02° | ✓
−1.0, 0.8, 90° | −1.010, 0.773, 90.08 | 2.9 cm · 0.08° | ✓
0.5, −0.5, −90° | 0.500, −0.469, −88.83 | 3.1 cm · 1.17° | ✓
· 11 unit tests on the control math — angle wrap, error geometry, saturation, slew.
· Live Gazebo runs + a headless kinematic sim for CI.
· Logging /cmd_vel confirms v and ω fire together — no rotate-drive-rotate.
· Repeatable from arbitrary start poses, sequential goals.
Notes: All three demo poses land inside tolerance — worst case about 3cm and just over a degree. Beyond the live runs, the control math has 11 unit tests, there's a headless kinematic sim for CI, and logging cmd_vel confirms v and omega fire together — no rotate-drive-rotate.

## Slide 10
09 / ASSUMPTIONS
Assumptions
Pose Controller
01
Odometry is reliable and low-drift over the short distances commanded.
02
Target pose is given in the same odom frame the robot starts in.
03
Flat, obstacle-free environment — this is pose control, not navigation or avoidance.
04
Differential-drive kinematics (TB3 burger) — no holonomic / lateral motion.
05
One goal serviced at a time — the service is blocking by design.
06
Platform limits approximated as TB3 burger maxima — 0.22 m/s, 2.84 rad/s.
Notes: Being explicit about the operating envelope. This is pose control, not navigation — flat, obstacle-free, reliable odometry, one goal at a time. The differential-drive model means no lateral motion.

## Slide 11
10 / LIMITATIONS & FUTURE WORK
Recommendation
Pose Controller
LIMITATION TODAY
IF WE TOOK IT FURTHER
No obstacle avoidance — straight / curved approach only (by scope).
Layer a local planner or reactive avoidance on top of the pose target.
Open to odometry drift over longer runs.
Fuse with AMCL / EKF to track a map frame.
Proportional law (terminal P on yaw); no integral term → small steady bias possible.
Mitigated by the settle window; add I / feed-forward if needed.
Fixed gains; cos(α) reverse is intentionally gentle.
Velocity-profile / trajectory for long goals; a dedicated backward-driving mode.
Notes: Honest about the edges. No obstacle avoidance by scope. Open to odom drift — a real deployment would fuse with AMCL or an EKF for a map frame. It's proportional with a terminal P on yaw — could add an integral term. And a dedicated reverse mode would beat the gentle cos-alpha reverse for goals behind the robot.

## Slide 12
11 / SUMMARY
→ Continuous polar controller — drives and rotates simultaneously.
→ Correct error computation — ρ / α / β with proper angle wrapping.
→ Clean ROS 2 structure — service + topics, parameterised, unit-tested.
→ Meets ±5 cm / ±5° on all three demo poses — no Nav2.
Repository & supporting materials submitted by email
Thank you — happy to dig into any part
Notes: The one-line takeaway - it curves onto the goal and stops on the mark. Continuous polar control, correct error computation, clean parameterised ROS 2 structure, tested, hitting tolerance on all three poses — all from first principles, no Nav2. Happy to walk through any part.